## Slide 1
Ruess 2026 – Applied Energy – 2026 Fraunhofer IPA – Universität Stuttgart
L1 - Copperplate | L2 - 7 aggregated Nodes | L3/L3+/L3NL - 15 Nodes
HP
CHP
Boiler
aggregated heat demand
HP
CHP
Boiler
Heat losses, Spatial structure
Transport delay, Pressure drop,
Temperature gradient
No losses, no spatial structure
Aggregated zone demand, steady-state losses
CHP
Boiler
HP
Full topolpgy resolution,
Different thermo-hydraulic physics
+ 10,5%
+ 13,0%
+ 13,1%
+ 13,5%
CO2
74 t CO2
underestimated
Topology Resolution Dominates Dispatch Accuracy in District Heating Networks with industrial loads:
A Five-Level MILP Comparison
Key findings
This study isolated 5 modeling dimensions for DH dispatch (topology and thermo-hydraulics). Casestudy for a heating grid (12MW, 8760h) and 36 synthetic grids.
topology dominates thermo-hydraulics
Copperplate underestimate cost by 13%
L1 | L2 | L3 | L3+ | L3NL
cumulative cost deviation from L1